## Slide 1: Lecture Title
Course Code: 0052
Dept. of Computer Science
Faculty of Science and Technology
Lecturer No: | 7 | Week No: | 7 | Semester: | 
Lecturer: | Name & email |  |  |  | 
Course Title: : Computer Organization and Architecture

## Slide 2: Overview : LOGIC
Instructions to change the bit pattern in a byte or word
The ability to manipulate bits manually which is unlikely in high level languages (Except C)
Logic Instructions: AND, OR, XOR and NOT
Logic Instructions can be used to clear, set, and examine bits, a register or variable. i.e. these will be used for
    Converting a lowercase letter to upper case
      Determining If a register contains an even or odd number.

## Slide 3: LOGIC
Instructions to change the bit pattern in a byte or word
The ability to manipulate bits manually which is unlikely in high level languages (Except C)
Logic Instructions: AND, OR, XOR and NOT
Logic Instructions can be used to clear, set, and examine bits, a register or variable. i.e. these will be used for
Converting a lowercase letter to upper case
Determining If a register contains an even or odd number.

## Slide 4: LOGIC Instructions
The ability to manipulate individual bits is one the main advantages of assembly language.
Individual bits can be changed in computer by using logic operations.
The binary values of 0 = False and 1= True
When a logic operation is applied to 8- or 16-bit operands, the result is obtained by applying the logic operation at each bit position.

## Slide 5: AND, OR, and XOR instructions
The AND, OR, and XOR instructions perform the named logic operations. The formats are:
    AND destination, source
    OR destination, source
    XOR destination, source
The result of the operation is stored in the destination, which must be a register or memory location.
The source may be a constant, register, or memory location.
However, memory-to-memory operations are not allowed.

## Slide 6: Effect on Flags
  SF, ZF, PF reflect the result
  AF is undefined
  CF, OF= 0
One use of AND, OR, and XOR is to selectively modify the bits in the destination.
To do this, we construct a source bit pattern known as mask.
The mask bits are chosen so that the corresponding destination bits are modified in the desired manner when the instruction is executed.

## Slide 7: MASK
To choose the mask bits, we make use of the following properties of AND, OR, and XOR:
The AND instruction can be used to CLEAR specific destination bits while preserving the others.
  A 0 mask bit clears the corresponding destination bit.
  a 1 mask bit preserves the corresponding destination bit.
The OR instruction can be used to SET specific destination bits while preserving the others.
  A 1 mask bit sets the corresponding destination bit.
  A 0 mask bit preserves the corresponding destination bit. ·
The XOR instruction can be used to complement specific destination bits while preserving the others.
  A 1 mask bit complements the corresponding destination bit;
  A 0 mask bit preserves the corresponding destination bit.

## Slide 8: Not Instruction
The NOT instruction performs the one's complement operation on the destination. The format is:
  NOT destination (**No effect on status flags)
  Example: Complement the bits in AX:
      NOT AX

## Slide 9: TEST Instruction
The TEST Instruction performs an AND operation of the destination with the source but does not change the destination contents.
The purpose of the test instruction is to set the status flags. The format is:
    TEST destination, Source
Effects of flags on test operation:
  CF, OF =0
  AF = Undefined
  SF, ZF, PF reflect the result

## Slide 10: Bit Examination on TEST
TEST instruction can be used to examine individual bits in operand.
The mask should contain 1's in the bit positions to be tested and 0’s elsewhere
    As 1 AND b = b, 0 AND b = 0
The operation TEST destination, mask
Will have 1's in the tested bit positions if and only if the destination has 1’s in these positions; and 0’s elsewhere.
if the destination has 0’s in all the tested positions, the result will be 0 and thus ZF=1

## Slide 11
References
Assembly Language Programming and Organization of the IBM PC, Ytha Yu and Charles Marut, McGraw Hill, 1992. (ISBN: 0-07-072692-2).
http://faculty.cs.niu.edu/~byrnes/csci360/notes/360shift.htm

## Slide 12
Books
Assembly Language Programming and Organization of the IBM PC, Ytha Yu and Charles Marut, McGraw Hill, 1992. (ISBN: 0-07-072692-2).
Essentials of Computer Organization and Architecture, (Third Edition), Linda Null and Julia Lobur
W. Stallings, “Computer Organization and Architecture: Designing for performance”, 67h Edition, Prentice Hall of India, 2003, ISBN 81 – 203 – 2962 – 7
Computer Organization and Architecture by John P. Haynes.